Menu design for transmitter.

1. Introduction
2. Concept of configuring a channel
3. Menu design (what’s needed)
4. Requirements to software

1. introduction

Before making any software that displays menus on the screen, a menu is designed.
It’s not the intention to make a final menu design, but to have good idea about what kind of menu elements we need, and what other programming constructs should be thought of.

Section 2 provides a concept design for the menu, with some notes with ideas, what is required, etc. Section 3 finally lists all requirements.
2. Concept of configuring a channel

Traditionally, transmitters have a lot of model programmed into them. E.g. by setting your transmitter to “mode 1” or “mode 2” determines almost completely which stick axis is coupled to which control surface on the plane. Maybe this is easier when just starting the hobby, but it has it’s quirks when you want some more advanced options, or when the model in the software does not exactly fit the plane that you want to fly. E.g. I read somewhere in a forum: “Does your transmitter support all the mixes that an advanced DLG setup needs?” which leads me to believe that most transmitters have a fixed set of mixes, and all you can changes are the parameters of each mix. Programming such a transmitter requires knowledge of (flying) the plane, and knowledge of the programming model inside the transmitter software.
I would like to have a transmitter that has as little “model” in it as possible. So, to me, it comes down to programming the mapping of the angle of rotation on a servo, based on the amount of movement of a particular stick on my transmitter.
So by removing all “model” form the transmitter I give myself a transmitter that might be a bit more tedious to program, but it’s much more transparent what happens at the output and why.

How to program a stick to servo mapping?
An output channel is programmed by having:
- a primary input
- a number of channel control elements, such as:
  - scale (multiple input signal by a factor)
  - dual rate (extra input from switch)
  - expo (exponential transfer function of stick to servo)
  - mixes (mix in signals from other inputs, output is sum of scaled inputs)

Having a simple structure like this keeps open possibilities like:
adding new config elements, such as:
- combinations, like dual rated expo
- new configuration elements, such as continuous variable rate (ie. “dual-rate” based on a potmeter input”)
3. Menu design

The current display I have is 128x64 pixels. Initially start with a simple text based menu. Good looking graphics are worth a lot, but for now I just want a working system.

If we use use a simple fixed-width font of 6x8 pixels per character,
then:
128/6 = 21.3 --> max 21 chars per line
64/8 = 8 lines

Initially we see screen with the model name and some parameter values like battery voltage, trim settings. In the future it would be nice to have some telemetry support as well, like: plane battery voltage, radio signal strenght, height, etc.
–> what is shown in the main screen should be configurable?

TBD.

Once the menu button is clicked the menu is shown.

The | and _ characters are drawn only to give some sense of the size of the display. It’s not the intention to show them.

 _____________________
| default_model back ← clickable items have some background color
|
| select model
| add model
|
|
|
|

Default model above should be the previous used model, for consistency. but in the beginning it’s probably easier to use the first one in storage.

<select model>
 _____________________
| select model back
|
| alula
| simulator
| x-ray micro
| apogee
|
|

<select model>, <alula> (i.e some model name)
 _____________________
| alula back
|
| edit name
| configure channels
| delete
| clone
|
|

<select model>, <alula>, <edit name>
 _____________________
| alula back
|
| alula_ ← the _ indicates a blinking cursor of a text field
|
|
|
|
|

store: <model name>

<select model>, <alula>, <configure channels>
 _____________________
| alula back
|
| edit channel1
| edit channel2
| edit channel3
| edit channel4
|
|

<select model>, <alula>, <configure channels>, <edit channel1>
 _____________________
| alula back
|
| rs_ud ---- ← right stick, up-down axis.
| |
| +
| |
| ---- CH1 ← might be nice to be able to name this channel (e.g. “pitch”)
|

Initially a channel is an empty pipe from a default input (or none? TBD) to the output.

You can click the input,rs_ud in this case, to change it. This is the primary input, other inputs can
be used for dual rate (probably a switch) and mixes.

<select model>, <alula>, <configure channels>, <edit channel1>, <+>, <rs_ud>
 _____________________
| alula back
|
| select input: ← ideally some sort of dropdown menu
| sw1
| sw2
| ls_ud
| ls_lr
| rs_ud
| rs_lr

store: channel config item.
Note: a channel configuration consists of a couple of elements. A primary input, some expo, dual rate, and a couple of mixers. For a first design an array of these elements should suffice. TBD: how to store different types of elements in an array? Possibly: use a tagged union data structure.

<select model>, <alula>, <configure channels>, <edit channel1>, <+>
 _____________________
| alula back
|
| add expo
| add dual_rate
| add mix
|
|

click <+>, <dual_rate>
 _____________________
| alula back
|
| dual rate settings
| switch: sw1 ← click, get dropdown menu to change
| high rate: 100% ← click, get blinking, up down to change value
| low rate: 80%
|
|

click <back>
 _____________________
| alula back
|
| rs_ud ----
| |
| +
| sw1 --- d_r
| +
| |
| ---- CH1
|

After adding an channel configuration element it is shown in the channel overview. We could go back and configure another channel, or add another element.

Other elements detailed out:

click <+>, <mix>

 _____________________
| alula back
|
| mixer settings:
| name: thr_to_flap ← text edit menu, for remebering what the mix is for
| scale pri: 80%
|
| mix in: ls_ud ← dropdown menu
| at scale: 20% ← numerical value click then up-down.
|

TBD: After adding a mix, is the final output 100% primary input + 100% mix input, so 200% deflection? My feeling is that the output of the mixer should be normalized to 100%. But how to do this? If mix in signal is scaled at 20%, and at flying time the input is zero (e.g. stick central position) then the primary input is scaled to 80%?
Make this explicit: add a scaling factor for both inputs. User knows and user decides.

_____________________
| alula back
|
| rs_ud ----
| |
| +
| sw1 --- d_r
| +
| ls_ud - mix
| +
| |
| ---- CH1
|

click <+>, <expo> note that you can now put expo at three different places, resulting in different behavior each!

 _____________________
| alula back
|
| expo settings:
| expo rate: 80% ← numerical value click then up-down.
|

Now after some configuring, we get to the something like this list:
_____________________
| alula back
|
| rs_ud ----
| |
| +
| sw1 --- d_r
| +
| ls_ud - mix
| +
| expo
| +
| |
| ---- CH1

There are now two things to deal with. First one is that the list becomes longer than the number of lines available in the screen. This means that we need scrolling functionality.

Second, what if we wanted to delete elements? This is solved by showing a delete option after clicking on the particular elment, e.g. click <expo>

 _____________________
| alula back
|
| expo settings:
| expo rate: 80% ← numerical value click then up-down.
|
| delete

A consequence of this choice is that we have a different function for adding and editing an element.
Or, there is flag stored somewhere, that “delete” is not shown when adding an element (as it would make no sense.)

4. Requirements to software

UI library

The user interface supports:
- display text strings (titles and stuff)
- buttons (back, delete, etc.)
- editable text field (click to start edit, up-down select char, click start editing char, up-down select char, click confirm, back to select char mode, up-down to “ok”, click leave editing mode.
- editable numeric field (click start edit, up-down change value, click leave editing mode.
- editable multivalue field (click start edit, up-down go to multi-values (dropdown ?), click leave edit.)
- scrolling down when there are more lines to show.